1st LAB AC
17/09/2024

Components of your computer:
- I / o
- Microprocessor
- Memory
- BUSes

when you code in C, you need a compiler, which converts the code in binary (instruction set), which is readable for the computer

TO DO: practice 2 complement (complemento para 2)

(open simulator - MARS)

/// to write script you define segments
/// the dot is directive “.”
/// the “#include” is an instruction
/// the memory cells are caled registers and are 32 bits long

.data

.text
.globl main
main:
/// li is load immediate
li $t0, 100
li $t1, 35
sub $t2, $t0, $t1	/// subtract value from t0 to value from t1 and store result in t2
addi $t3, $t2, 50	/// add 50 to t2 and store result in register t3

/// to simulate a for cycle ©, we use BNE (branch if not equal, in Assembly)

ex: bne $s2, $s0, loop

/// if s2 is not equal to s0, go back to main
ex code Assembly:
loop:
add $t1, $t1, $t0
addi $t0, $t0, 1
bne $t0, $t2, loop

(alternative)
loop:
biq $t0, $t2, exit	/// branch if equal
add $t1, $t1, $t0
addi $t0, $t0, 1
j loop	/// jump loop – goes back to beginning
exit

system calls
example:
.data
tab:	.word 1, 2, 3, 4

.text
.global main
main:
li $v0, 5	// in sytem call, the value 5 stands for read int, and reads input from user
syscall

la $t0, tab	// load address with the first value in the table, works like a pointer
lw $t1, 4($t0)	// loads t1 with second value in table (t0)
add $a0, $v0, $t1

addi $a0, $v0, 50
li $v0, 1
sycall

comparação C – Assembly

C:
if($t1 = $t2)
$t3 = $t1;
else
$t3 = 0;

Assembly:
biq $t1, $t2, do
move $t3, $zero
j exit
do: move $t3, $t1
exit: